Lab 5 Worksheet

The following questions are worth 1 point each.

1. For what values of the “Sum” register will the Z code be set to 1?
0

2. In signed format, what is a decimal value of the Sum register for which the N bit is set to 0?
1

3. In unsigned format, what is a decimal value of the Sum register for which the N bit is set to 0?
1

4. Why is the carry-in bit set to 1 during subtraction?
in case the subtraction of two numbers requires a borrow in the
leftmost bits

For the following table, perform the arithmetic assuming unsigned 4-bit registers and fill in the conditional codes based on the sum. Each cell is worth 1 point (56 total points). Use the completed GUI binary adder to help you. Note: subtraction is performed using 2’s Complement however you should still put the positive value in the cells.
Decimal		Binary
10		1010
+ 3		+11
= 13		=1101
N	Z	V	C
1	0	0	0

Decimal		Binary
7		0111
+7		+ 0111
= 14		=1110
N	Z	V	C
1	0	1	0

Decimal		Binary
12		1100
-5		-0101
= 7		= 0111
N	Z	V	C
0	0	1	0

Decimal		Binary
10		1010
-6		-0110
= 4		= 0100
N	Z	V	C
0	0	1	0

Now assume signed arithmetic (still 4-bit registers).

Decimal		Binary
4		0100
+ 3		+0011
= 7		= 0111
N	Z	V	C
0	0	0	0

Decimal		Binary
4		0100
+ -6		+ 1010
= -2		= 1110
N	Z	V	C
1	0	0	0

Decimal		Binary
4		0100
- -6		- 1010
= -6		= 1010
N	Z	V	C
1	0	1	1